## Slide 1
Autonomous Drones and Perception
RoverTech
[R]overTech x Polispace x Suncubes Workshop
Federico De Donatis
Luca Attorrese
RoverTech
[ ]
R

## Slide 2
FROM MEASUREMENTS TO ATTITUDE
RoverTech
Lesson 2
Sensors, Observability and Sensor Fusion

## Slide 3
Federico De Donatis
Systems architecture & avionics integration
Your Speakers
Robotics and perception
Luca Attorrese

## Slide 4
Material
FedericoDD/workshop-PX4/

## Slide 5
Workshop Map
Lesson 1
Lesson 3
Lesson 2
ESTIMATE
PERCEIVE
BUILD
Hardware, PX4
IMU + EKF
Camera +
Visual Odometry
07/10
14/10
21/10

## Slide 6
Frames
Attitude arrives as a quaternion
EXPLAINED IN LESSON 2
ATTITUDE ESTIMATOR
fuses IMU and other aiding sources
INVERSE ROTATION
rotate NED gravity back into BODY
BODY GRAVITY
uORB topic with the current attitude
Hamilton quaternion, FRD → NED
Forward, Right, Down components
vehicle_attitude
Don't confuse the two operations
The estimator creates the attitude; gravity_demo only reads it and changes coordinates.

## Slide 7
Frames
Attitude arrives as a quaternion
ATTITUDE ESTIMATOR
fuses IMU and other aiding sources
INVERSE ROTATION
rotate NED gravity back into BODY
BODY GRAVITY
uORB topic with the current attitude
Hamilton quaternion, FRD → NED
Forward, Right, Down components
vehicle_attitude
Don't confuse the two operations
The estimator creates the attitude; gravity_demo only reads it and changes coordinates.

## Slide 8
Estimation
What does estimation mean?
x̂
z
Infer a hidden state from measurements, a model and uncertainty.

## Slide 9
Estimation
What does estimation mean?
x̂
z
Infer a hidden state from measurements, a model and uncertainty.

## Slide 10
Estimation
What does estimation mean?
Infer a hidden state from measurements, a model and uncertainty.
MEASUREMENT
z
What sensors provide about the physical system.
MODEL
f, h
How the state evolves and produces measurements.
STATE ESTIMATE
The best current inference of the hidden state.

## Slide 11
One attitude-estimation example
MEASUREMENT
Measured angular rate
Reference: J. Solà (2017), Quaternion kinematics for the error-state Kalman filter.

## Slide 12
One attitude-estimation example
MEASUREMENT
Measured angular rate
MODEL
Remove estimated bias
Reference: J. Solà (2017), Quaternion kinematics for the error-state Kalman filter.

## Slide 13
One attitude-estimation example
MEASUREMENT
Measured angular rate
MODEL
Remove estimated bias
STATE ESTIMATE
Compose small rotations
x
Reference: J. Solà (2017), Quaternion kinematics for the error-state Kalman filter.

## Slide 14
Quaternion integration
Reference: J. Solà (2017), Quaternion kinematics for the error-state Kalman filter.
Gyro rate becomes a sequence of small rotations
1 CORRECT THE RATE; INTEGRATE OVER Δt
2 MAP THE ROTATION VECTOR TO δq
3 COMPOSE AND REPEAT
Each new gyro sample adds one small rotation to the current attitude.
4 NORMALIZE

## Slide 15
MEASUREMENT
RoverTech

## Slide 16
Measurement
A sensor translates physics into electricity
PHYSICAL STIMULUS
SENSOR
ELECTRICAL SIGNAL
“A sensor is a device that receives a stimulus and responds with an electrical signal.”
Academic definition: J. Fraden, Handbook of Modern Sensors.

## Slide 17
Sensors
What is a sensor?
PHYSICAL QUANTITY
TRANSDUCER
ANALOG SIGNAL
CONDITIONING + ANTI-ALIAS
ADC
DIGITAL MEASUREMENT
Conceptual chain: transduction → conditioning → sampling → digital measurement

## Slide 18
Sensors
How do I choose a sensor?
DYNAMIC WINDOW
RANGE
BANDWIDTH
ODR / SAMPLE RATE
Terminology aligned with PX4 v1.17 sensor and estimator integration documentation.

## Slide 19
Sensors
How do I choose a sensor?
ERROR BEHAVIOUR
NOISE
BIAS
LATENCY
Terminology aligned with PX4 v1.17 sensor and estimator integration documentation.

## Slide 20
Sensors
How do I choose a sensor?
INTEGRATION
INTERFACE
POWER
MASS
ENVIRONMENT
Terminology aligned with PX4 v1.17 sensor and estimator integration documentation.

## Slide 21
Sensors
How do I choose a sensor?
DYNAMIC WINDOW
RANGE
BANDWIDTH
ODR / SAMPLE RATE
ERROR BEHAVIOUR
NOISE
BIAS
LATENCY
INTEGRATION
INTERFACE
POWER
MASS
ENVIRONMENT
Which specification affects estimation quality?
Almost all of them, but in different ways.
Terminology aligned with PX4 v1.17 sensor and estimator integration documentation.

## Slide 22
MODEL
RoverTech

## Slide 23
Sensors
The minimum measurement model
h(x)
IDEAL RELATIONSHIP
how the hidden state creates the measurement
b
BIAS
a persistent offset that looks like truth
n
RANDOM NOISE
unpredictable variation around the measurement
reality adds more: scale factor · misalignment · saturation · latency
Notation follows standard estimation and inertial-navigation measurement models.

## Slide 24
Sensors
Gyroscope
TRUE ANGULAR RATE
+ tiny bias
INTEGRATE
rate → attitude
Rate-gyro model with additive bias and noise · Markley & Crassidis; Groves

## Slide 25
Sensors
Accelerometer
Doesn’t measures roll, pitch or attitude but a specific force.
LOW DYNAMIC ACCELERATION
gravity direction becomes useful → tilt can be constrained
WHAT IF THE DRONE ACCELERATES FORWARD?
specific force is no longer ‘just gravity’ → the model separates motion from gravity
Sensor fusion needs a model because the same measurement can have different causes.
Specific-force convention: standard strapdown inertial navigation · Groves; Markley & Crassidis

## Slide 26
Sensors
Magnetometer
It measures the magnetic-field vector (not the yaw!).
REFERENCE
field direction may constrain heading
Vector observation model for attitude determination · Shuster; Markley & Crassidis

## Slide 27
Sensors
Magnetometer
It measures the magnetic-field vector (not the yaw!).
REFERENCE
field direction may constrain heading
CORRUPTION
motors · current · nearby ferromagnetic material
Vector observation model for attitude determination · Shuster; Markley & Crassidis

## Slide 28
Sensors
9-DoF IMU or 6-DoF + remote mag?
Both: 3 gyro + 3 accel + 3 magnetic axes
Same axes; different magnetic exposure and integration effort.
9-DOF INTEGRATED MODULE
PRO: Compact; fewer cables
CON: Fixed mag location can limit isolation from motors and power wiring.
6-DOF IMU + REMOTE MAG
PRO: Place mag away from current
CON: More wiring; align frames and manage timing/calibration.
Sources: Bosch Sensortec, BNO055; PX4, Mounting a GPS/Compass.

## Slide 29
Sensors
Allan variance reveals sensor noise by time scale
Sources: NIST, Time and Frequency from A to Z; MathWorks, Inertial Sensor Noise Analysis Using Allan Variance.
COMPARE ADJACENT TIME WINDOWS
The Allan variance (AVAR), also known as two-sample variance, is a measure of frequency stability in clocks, oscillators and amplifiers. Record a stationary gyro or accelerometer ():
The M-sample variance is a measure of frequency stability using M samples, time T between measurements and observation time

## Slide 30
Sensors
One state, many sources
ATTITUDE
←
GYRO
GRAVITY
MAGNETIC FIELD
VISION
HEIGHT
←
BAROMETER
GNSS
RANGE
VISION
HORIZONTAL MOTION
←
GNSS
OPTICAL FLOW
VIO

## Slide 31
Sensors
One state, many sources
ATTITUDE
←
GYRO
GRAVITY
MAGNETIC FIELD
VISION
HEIGHT
←
BAROMETER
GNSS
RANGE
VISION
HORIZONTAL MOTION
←
GNSS
OPTICAL FLOW
VIO
If every sensor is incomplete, maybe the information is in the combination.
SENSOR FUSION

## Slide 32
Sensors
WHY ONE SENSOR IS NOT ENOUGH

## Slide 33
Sensors
WHY ONE SENSOR IS NOT ENOUGH

## Slide 34
Sensors
WHY ONE SENSOR IS NOT ENOUGH
GYROSCOPE
good short-term angular information
but bias causes drift
ACCELEROMETER
gravity reference for tilt
but dynamic acceleration corrupts it
MAGNETOMETER
heading information
but magnetic disturbances corrupt it
No sensor is wrong BUT no sensor is enough.

## Slide 35
ESTIMATION
RoverTech

## Slide 36
Estimation
SENSOR FUSION
No sensor is wrong BUT no sensor is enough.
GYROSCOPE
ACCELEROMETER
MAGNETOMETER
STATE ESTIMATE
Combine complementary measurements according to their uncertainty.
When model and measurements disagree, who should we trust?

## Slide 37
Estimation
FROM KALMAN TO FLIGHT
RUDOLF E. KALMAN
1960
Recursive state-estimation framework
STANLEY F. SCHMIDT
EARLY AEROSPACE APPLICATIONS
Implementation and practical nonlinear navigation work at NASA Ames
A mathematical idea became an engineering tool because aerospace needed navigation in the real world.
MODEL + MEASUREMENT + UNCERTAINTY
KALMAN FILTER

## Slide 38
Estimation
APOLLO GUIDANCE COMPUTER
CPU 2 MHz (16-bit) - RAM 4 KB - ROM 74 KB - Peso 32 kg - Consumo 55W

## Slide 39
Estimation
AN ESTIMATE IS NOT JUST A NUMBER
best current state estimate
covariance / uncertainty associated with the estimate

## Slide 40
Estimation
AN ESTIMATE IS NOT JUST A NUMBER
best current state estimate
covariance / uncertainty associated with the estimate

## Slide 41
Estimation
THE KALMAN FILTER IN TWO VERBS
PREDICT
MODEL
CORRECT
MEASUREMENT MODEL
PREDICT
MODEL
CORRECT
MEASUREMENT MODEL
If prediction and measurement disagree, who wins?
Neither automatically.
The less uncertain information gets more authority.
MEASUREMENT
MEASUREMENT

## Slide 42
Estimation
PREDICT
STATE
Where does the model think we moved?
UNCERTAINTY
How uncertain did we become while moving?
Q
What uncertainty in the evolution does the model admit?
Prediction moves both the estimate and its uncertainty.

## Slide 43
Estimation
INNOVATION
WHAT I MEASURED
−
WHAT I EXPECTED TO MEASURE
If the innovation is unexpectedly large, is the sensor wrong, the model wrong, or both?

## Slide 44
Estimation
CORRECT
LARGE R
measurement gets less authority
LARGE P⁻
measurement gets more authority
Kalman filtering is uncertainty-aware feedback on information.

## Slide 45
Estimation
SO WHY “EXTENDED”?
NONLINEAR MODEL
LOCAL LINEAR VIEW
The EKF does not make the world linear. It linearises our uncertainty locally around the current estimate.

## Slide 46
Estimation
FROM CONTINUOUS DYNAMICS TO F
FORWARD EULER
IDENTIFY F
With constant A, the exact transition is F = exp(AΔt).

## Slide 47
Estimation
DIFFERENT PHYSICS, DIFFERENT ESTIMATORS
BEYOND TODAY
MEKF / ERROR STATE
local attitude-error representation
AUGMENTED STATE
biases / coloured stochastic processes
UKF
sigma-point propagation through nonlinear mappings
DUAL / JOINT ESTIMATION
states + parameters
TOBIT / CENSORED FILTERING
censored or saturated measurements
Different physics can require different states, stochastic models and approximations.

## Slide 48
Quaternions
DEFINITION · SCALAR-FIRST CONVENTION
q = [q₀; q₁, q₂, q₃]
q₀ = cos(θ/2)
[q₁,q₂,q₃] = u sin(θ/2)
θ = rotation angle, ‖u‖ = 1 , ‖q‖ = 1
PRO / WHY USE THEM
No Euler-angle gimbal lock; small rotations compose with ⊗.
CONS / WHAT TO MANAGE
4 values for 3 DOF; renormalize. q and −q encode the same rotation.
Source: J. Solà (2017), Quaternion kinematics for the error-state Kalman filter.
STATE ESTIMATE
Compose small rotations
x

## Slide 49
Quaternions
DEFINITION · SCALAR-FIRST CONVENTION
q = [q₀; q₁, q₂, q₃]
q₀ = cos(θ/2)
[q₁,q₂,q₃] = u sin(θ/2)
θ = rotation angle, ‖u‖ = 1 , ‖q‖ = 1
Source: J. Solà (2017), Quaternion kinematics for the error-state Kalman filter.
STATE ESTIMATE
Compose small rotations
x
DEFINITION · SMALL ROTATIONS

## Slide 50
Estimation
PREDICT WITH THE GYROSCOPE
GYRO
REMOVE ESTIMATED BIAS
INTEGRATE ROTATION
PREDICT ATTITUDE
Excellent short-term information. But prediction alone drifts.

## Slide 51
Estimation
OUR MINIMAL ESTIMATOR
attitude correction
gyro-bias correction
GYRO
PREDICT
ACCELEROMETER
CORRECT TILT
MAGNETOMETER
AID HEADING
Let’s start with prediction.

## Slide 52
Estimation
GRAVITY COMES BACK
LESSON 1
gravity in NED
rotate into BODY
measurement model
GRAVITY IN NED
PREDICTED GRAVITY IN BODY
ACCELEROMETER
information compatible with gravity
when dynamic acceleration is sufficiently compatible with the model
The coordinate transformation from Lesson 1 has become a measurement model.

## Slide 53
Estimation
SOMETHING IS STILL MISSING
Gyroscope + accelerometer. Do we now know full attitude?
ROTATE AROUND GRAVITY
ROLL
constrained by gravity
PITCH
constrained by gravity
YAW
not absolutely constrained by gravity
Rotating around gravity does not change the gravity vector.

## Slide 54
Estimation
GIVE HEADING A REFERENCE
So what information could constrain heading?
MAGNETIC FIELD
MAGNETOMETER
magnetic-field vector
OUR EDUCATIONAL ESTIMATOR
VISION
External vision / VIO
external geometric reference
GNSS-BASED HEADING
suitable hardware + geometry
heading information when observable

## Slide 55
Navigation
What is still missing?
WHERE IT IS
HOW FAST IT MOVES
HOW IT IS ORIENTED
A drone may know
its own state
What does it know about the world around it?
PERCEPTION
CAMERA
DEPTH
LiDAR
LESSON 3
Navigation estimates the vehicle. Perception interprets the environment.

## Slide 56
Navigation
How high are we?
BAROMETER
MEASURES static pressure
USEFUL smooth relative height
LIMIT weather + propwash drift
GNSS
MEASURES signal travel time
USEFUL global altitude outdoors
LIMIT noise · geometry · outages
RANGEFINDER
MEASURES distance to a surface
USEFUL low altitude + landing
LIMIT range + surface geometry
EXTERNAL VISION
MEASURES image features / pose
USEFUL prepared environments
LIMIT lighting · coverage · latency
Height is a state. Each sensor observes it differently.
One physical quantity · four incomplete information sources

## Slide 57
Navigation
How fast are we moving sideways?
GNSS VELOCITY
Measures change in the global navigation solution
Best when: open sky + global reference
Watch: geometry · outages · latency
OPTICAL FLOW
Measures apparent image motion over the ground
Best when: texture + known height
Watch: lighting · altitude · surface
VIO / EXTERNAL VISION
Combines visual motion with inertial or external pose
Best when: GNSS is weak or unavailable
Watch: compute · calibration · drift
Velocity sources answer different questions under different operating conditions

## Slide 58
PX4
RoverTech

## Slide 59
Navigation
How does a measurement reach PX4?
SENSOR
physical measurement
INTERFACE
SPI · I²C UART · CAN
DRIVER
read · timestamp calibrate · publish
uORB
typed software topic
MODULE
subscribe check · fuse
Official PX4 v1.17 docs · Drivers publish sensor data through uORB; interface depends on device and bus

## Slide 60
Estimation
OUR FILTER IS NOT PX4 EKF2
OUR EDUCATIONAL FILTER
ATTITUDE
GYROSCOPE BIAS
ACCELEROMETER AIDING
MAGNETOMETER AIDING
small enough to see every idea
PX4 EKF2
FULL NAVIGATION ESTIMATOR
ATTITUDE · VELOCITY · POSITION
SENSOR BIASES
MULTIPLE AIDING SOURCES
real navigation scope

## Slide 61
Estimation
PREDICTION: FROM GYROSCOPE TO STATE TRANSITION
R(q): BODY/FRD → NED
B - LINEAR MODEL
A RIGHT-MULTIPLICATIVE LOCAL ERROR
Attitude error:
Linearization:
=
C – DISCRETE LINEAR MODEL
Notes: ~90 seconds. Define gyro measurement omega_m=omega+b_g+n_g in rad/s; the code receives vehicle_imu.delta_angle in radians, dt=delta_angle_dt·10^-6 seconds, then forms measured rate dangle/dt after deliberately adding kDemoYawBiasRadS·dt to its z increment (+0.5 degree/s for the demo). Let delta-b=b_true-b_hat, q_true≈q_hat⊗delta_q(delta-theta), and omega_hat=omega_m-b_hat. With a right-multiplicative BODY-frame small error, differentiating q_true=q_hat⊗delta_q and keeping first-order terms yields delta-dot-theta≈-[omega_hat]_cross delta-theta-delta-b-n_g; bias error is modelled as a random walk, delta-dot-b≈w_b. Thus A=[-[omega_hat]_cross,-I3;0,0], the upper-right -I3 dt in F makes bias error accumulate as attitude error. The actual implementation constructs F by subtracting skew(rate)·dt in its upper-left block and setting F[i][i+3]=-dt. It uses F≈I+A dt and P_minus=F P_plus F^T+Q_k; Q_k is a first-order diagonal approximation, not an exact matrix exponential/discretization. The nominal estimate uses q_hat_minus=q_hat_plus⊗Exp_q(omega_hat dt), implemented with Q4::delta(rate*dt) and normalization in AttitudeFilter::predict(). The body-to-NED quaternion is unit norm; Exp_q(dtheta)=[cos(|dtheta|/2),sin(|dtheta|/2) dtheta/|dtheta|], with its small-angle branch. Bias estimate is held constant in prediction. This is kinematics driven by measured angular motion: no rigid-body inertia or torque equation.
DERIVATION — RIGHT-MULTIPLICATIVE BODY ERROR
R_true = R_hat Exp([δθ]×), E = R_hatᵀ R_true ≃ I + [δθ]×. Here R maps BODY/FRD to NED, and δθ is a BODY-frame right-multiplicative local error. With Ṙ_true = R_true[ω_true]× and Ṙ_hat = R_hat[ω_hat]×, differentiating E gives Ė = −[ω_hat]× E + E[ω_true]× exactly.
The measured gyro reads ω_m = ω_true + b_g,true + n_g, while ω_hat = ω_m − b_hat_g. Define δb_g = b_g,true − b_hat_g; therefore ω_true = ω_hat − δb_g − n_g. Substitute E ≃ I+[δθ]× into Ė and retain first-order terms: [δθ̇]× = −[ω_hat]×[δθ]× + [δθ]×[ω_hat]× − [δb_g+n_g]× = −[ω_hat×δθ]× − [δb_g+n_g]×.
Consequently δθ̇ = −[ω_hat]×δθ − δb_g − n_g. If the nominal bias is held constant and true bias is a random walk, δḃ_g = w_b. For δx=[δθ;δb_g], A has 3×3 blocks Aθθ=−[ω_hat]×, Aθb=−I₃, Abθ=0, Abb=0; w=[−n_g;w_b]. The upper-right minus sign follows δb_g=b_true−b_hat: overestimating bias lowers ω_hat and makes the true-minus-nominal attitude error grow. Left-multiplicative or nominal-minus-true error conventions change signs; do not mix them. F≈I₆+AΔt and P⁻=FP⁺Fᵀ+Q are covariance prediction, not propagation of the unknown true δx.

## Slide 62
Estimation
ACCELEROMETER: THE FIRST MEASUREMENT MODEL
PHYSICS
QUASI-STATIC:
Notes: ~75 seconds. An accelerometer senses specific force f^B=R(q)^T(a^N-g^N), not acceleration a^N directly: at rest in NED g^N=(0,0,+9.80665 m/s²) and a^N≈0, so f^B≈-R(q)^T g^N. Code bridge: attitude_lab.cpp constructs specific_force=imu.delta_velocity/dt_acc, where dt_acc=imu.delta_velocity_dt×10^-6 s; attitude_filter.hpp correct_accel() forms z_a=f^B/||f^B|| and h_a(q_hat)=q_hat.inverse_rotate((0,0,-1))=R(q_hat)^T(0,0,-1). For right-multiplicative q_true≈q_hat⊗delta_q(delta-theta), R(q_true)^T g≈(I-[delta-theta]_cross)h≈h+[h]_cross delta-theta, giving H_a=[[h_a]_cross,0_(3×3)] with a positive skew(h) block, exactly the implemented update_vector() Jacobian. The innovation is nu_a=z_a-h_a. Gravity is invariant to rotations about its own direction, so this observation alone does not fix yaw. The implementation rejects ||f|| outside [0.85g,1.15g] and normalized innovation norm >0.7; these are heuristic gates and do not prove absence of translational acceleration. During acceleration, a^N is nonzero and interpreting normalized specific force as gravity biases tilt. R(q) is a rotation matrix, while R_a denotes measurement noise covariance; q_hat^- and q_hat^+ are pre- and post-correction estimates. The 0.07²I₃ covariance is in normalized-vector units, not (m/s²)².

## Slide 63
Estimation
MAGNETOMETER: MAKING YAW OBSERVABLE
PHYSICS
Notes: ~75 seconds. An accelerometer senses specific force f^B=R(q)^T(a^N-g^N), not acceleration a^N directly: at rest in NED g^N=(0,0,+9.80665 m/s²) and a^N≈0, so f^B≈-R(q)^T g^N. Code bridge: attitude_lab.cpp constructs specific_force=imu.delta_velocity/dt_acc, where dt_acc=imu.delta_velocity_dt×10^-6 s; attitude_filter.hpp correct_accel() forms z_a=f^B/||f^B|| and h_a(q_hat)=q_hat.inverse_rotate((0,0,-1))=R(q_hat)^T(0,0,-1). For right-multiplicative q_true≈q_hat⊗delta_q(delta-theta), R(q_true)^T g≈(I-[delta-theta]_cross)h≈h+[h]_cross delta-theta, giving H_a=[[h_a]_cross,0_(3×3)] with a positive skew(h) block, exactly the implemented update_vector() Jacobian. The innovation is nu_a=z_a-h_a. Gravity is invariant to rotations about its own direction, so this observation alone does not fix yaw. The implementation rejects ||f|| outside [0.85g,1.15g] and normalized innovation norm >0.7; these are heuristic gates and do not prove absence of translational acceleration. During acceleration, a^N is nonzero and interpreting normalized specific force as gravity biases tilt. R(q) is a rotation matrix, while R_a denotes measurement noise covariance; q_hat^- and q_hat^+ are pre- and post-correction estimates. The 0.07²I₃ covariance is in normalized-vector units, not (m/s²)².

## Slide 64
Estimation
UNCERTAINTY PRODUCES THE KALMAN CORRECTION
MATRIX | CURRENT ASSUMPTION | ROLE
 |  | initial rotation error
 |  | initial gyro-bias error
 |  | process / rotation
 |  | process / gyro bias
 |  | normalized acceleration
 |  | normalized magnetic field
MATRIX | CURRENT ASSUMPTION | ROLE
 |  | initial rotation error
 |  | initial gyro-bias error
 |  | process / rotation
 |  | process / gyro bias
 |  | normalized acceleration
 |  | normalized magnetic field
INNOVATION
UNCERTAINTY
GAIN
ERROR UPDATE
The Kalman gain is not manually tuned: it emerges from our uncertainty models.
Notes: ~90 seconds. For either unit-vector observation, residual nu=z-h(q_hat^-), H=[[h]_cross,0] has size 3×6, covariance P^- is 6×6 and R is 3×3, so innovation covariance S=H P^- H^T+R is 3×3. Gain K=P^- H^T S^-1 is 6×3; delta-x_hat=K nu splits into delta-theta_hat (first three) and delta-b_hat (last three). In attitude_filter.hpp update_vector(), ekf=ekf*Q4::delta(delta-theta_hat), normalize, bias=bias+delta-b_hat. The attitude correction is clipped to magnitude 0.25 rad to preserve the local approximation. For numerical stability covariance is first updated by Joseph form P_J=(I-KH)P^-(I-KH)^T+K R K^T (code variable M and N). After injecting the error, reset its mean to zero and transform covariance with reset Jacobian G≈diag(I3−0.5[delta-theta_hat]_cross,I3); the implementation symmetrizes P=0.5(G P_J G^T+(G P_J G^T)^T). Verify source values: constructor P0=diag(0.15²I3,0.04²I3); predict() Q_k=diag((0.02² Δt)I3,(0.002² Δt)I3); correct_accel() passes sigma=0.07, correct_mag() sigma=0.08, so R_a=0.07²I3, R_m=0.08²I3. Q is a first-order discrete approximation to diagonal spectral densities, with no cross-terms; the values are educational guesses, not sensor statistics identified from Allan variance, datasheets or SITL recordings. Both observation vectors are normalized, hence R_a and R_m apply to unit-vector residuals, not raw m/s² or Gauss. Proper engineering tuning compares innovation consistency and ground-truth attitude/bias in controlled SITL cases after sensor characterization. Distinguish R(q) rotation from R_a/R_m covariance, and predicted x_hat^- from corrected x_hat^+.

## Slide 65
Material
FedericoDD/workshop-PX4/

## Slide 66
Recap
UNDERSTAND WHAT IS A SENSOR
BUILD THE PREDICT / CORRECT LOGIC
EXPLAIN WHY WE NEED SENSOR FUSION

## Slide 67
Next time
Lesson 1
Lesson 3
Lesson 2
ESTIMATE
PERCEIVE
BUILD
Hardware, PX4
IMU + EKF
Camera + Visual Odometry
07/10
14/10
21/10

## Slide 68
Thank you!
RoverTech